## Slide 1: H4.4 - Summary of chapters 7.1 and 7.2 Of the thesis “Ansatz für ein prozessintegriertes Qualitätsregelungssystem für nicht stabile Prozesse“ Hans Dörmann Osuna
by Kevin Kretschmar
and Krister Wolfhard

## Slide 3: Classic quality control loop (reactive)
Serves the timely detection and control of deviations
Backwards chained
  Measures do not affect the currently produced part
Process parameters are statistically evaluated
  Recommended action is derived
Control variables of the parameters must be measurable and processable
  z.B. temperature, pressure, ...

## Slide 4: Data evaluation
Takes place on the basis of decision-support systems
  based on machine learning methods
    E.g. decision trees
  Data is prepared using data mining methods
Data Understanding
  Data set with required variables is created
Data Preparation
  Data record is prepared as required
    Table with input and target values
    Data may be summarized in sections

## Slide 5: Data evaluation II
Modeling and data analysis
  Modeling through decision trees based on the data set
    CART/CHAID decision trees
Implementation
  New target specifications are generated by models
  Existing specifications are adjusted
  Rules derived from the model are confirmed/refuted

## Slide 6: Predictive dynamic testing
Same target parameterization of the systems as at the time of model creation
No changes in the general conditions (i.e. change of tools), as these influences would not be included in the models
Same environmental conditions as at the time of modeling
Change of general conditions → Anpassung des Modells
Based on existing process and quality data
Classification into three quality categories:
  Components that are highly likely to be good
  Components that are highly likely to be defective
  Parts that cannot be clearly classified

## Slide 8: Forward quality control loop
Base data for predictive testing:
  Historic data for model creation
  Current production data for prediction
  Current data for testing models
Historic Data → Classification of parts

## Slide 9: Methods of predictive dynamic testing
Interactive procedures
Non-interactive procedures cannot be changed accordingly
All methods split data sets into training data and test data
CART decision tree
CART decision tree with defined Misclassification costs
CHAID decision tree
C 4.5 decision tree
C 4.5 decision tree with different Pruning-settings
Binary logistic regression
neural networks

## Slide 10: Methods of predictive dynamic testing
Results of the methods can be "if-then-rules" or mathematical equations
Future components receive calculation fields that are used to determine the probability
Threshold values to determine the category